## Slide 1: Ag Sensors for the Measurement of Soil Water Contents
Team: sdmay18-38
Advisor: Dr. Dong
Client: Iowa State University

## Slide 2: Project Goal
Improve soil sensors created by Dr. Liang Dong and his research team
  Measure nitrogen levels within soil water content
  Displays data through phone application
Application
  Farmers
  Researchers

## Slide 3: Requirements
Functional
  Portable
  Low maintenance
  Data collection via phone application
Nonfunctional
  Intuitive software
  Easy to operate hardware
  Cheap for consumers

## Slide 4: Design Improvements
  Our group focused on three main areas to improve, those being:
  Sensors
    Design and Fabrication
  Control box
    Circuit and Box Manufacturing
  Software
    Phone Application and Server

## Slide 5: Sensors
Purpose: To measure the voltage potential of soil water in order to determine the nitrogen concentration.
Reference and working electrodes

## Slide 6: Sensors Previous Design
Features:
  Copper Solder Pads
  Silver Strip for chemical deposition
  (working and reference electrodes)
Flaws:
  Small area for chemical deposition
  Sensor boards were rectangular instead of circular.
  Corrosion on sides of copper
  Conductivity issue from silver strips to solder pads

## Slide 7: Sensor Previous Design: Flaws

## Slide 8: Sensors Current Design
Features:
  Copper solder pads
  Circular chemical deposition pads
  Solder mask
  Temperature Sensor on back side of PCB
Improvements:
  Corrosion protection
  Larger solder pads
  Easier chemical deposition
  Temperature sensing

## Slide 9
Testing: Took place in Coover labs
  Nitrogen levels
    Test range from 1-100 PPM
  Temperature
    Tests were performed over three different temp ranges
  Procedure
    Dilute nitrogen solutions
    Insert sensor electrodes into solution for 2 minutes
    After 2 minutes record the voltage
    Rinse sensor in distilled water
    Wait 2 minutes
    Perform another test
Sensor Testing

## Slide 10
Sensor Testing Results – Room Temp

## Slide 11: Sensor Testing Results – Room Temp

## Slide 12
Sensor Testing Results – Alternate Temp

## Slide 13: Control Box
Purpose:
  The control box serves as a bridge between the sensors and software by aiding in data processing
Components:
  New voltage amplification circuit
  Battery
  External 16 bit ADC
  Battery charger
  Power boost
  New switch for on/off modes
  Microcontroller

## Slide 14: Voltage Amplification Circuit
Purpose: Capture voltage between sensor electrodes and transmit to microcontroller
Changes: Added battery charger to circuit to reduce overall size
  Ultiboard (New design)
  Multisim (New design)
  Soldering
Other iterations:
  Tried adding voltage boost circuit as well
  Op-amps on both sides

## Slide 15: Amplifier Circuit PCB Before & After

## Slide 16: Physical Box Changes
New switch for on/off modes
Manufacturing via ETG / Boyd Lab
  Autodesk Inventor
  Several iterations
    Different boxes
    Errors

## Slide 17: Software
Purpose: Provide a means for pulling the raw value and processes the data, store the data and present it to the user.
Changes: MCU Code Rewritten, all other new
Integrations: Offline only app

## Slide 18: System Architecture

## Slide 19: Server
Data Storage
CSV download
Written with Node.js and Mongo DB
Scalable
Can be run on any platform
Easy to implement new features

## Slide 20: Software Demo

## Slide 22: Future Improvements
Sensors:
  Ion Selective Membrane
  Adaptability for other chemicals
Control box:
  Waterproofing
  Further size reduction
Software:
  Make an Apple App
  Extend Server Interface

## Slide 23: Special Thanks
Thank you for your time!
We would also like to thank:
  Project advisor and client Dr. Liang Dong
  Graduate students Xinran Wang and Yuncong Chen
  Dr. Azahar Ali
  Dr. Michael Castellano